## Slide 1: OREGON DOT STATUS OF PROFILER CERTIFICATION PROGRAM & CONTRACT SPECIFICATIONS
Mike Stennett, PE
Assistant Pavement Materials Engineer
RPUG 2012

## Slide 2: Timeline
2010 - First IRI Specifications on Contracts by Contract Change Order
2011 – Interstate Smoothness Specifications IRI only
2012 - Goal - only IRI specification to be used for Smoothness on HMAC with a Schedule 1 & Schedule 2
2013 - Spec Revisions, Possibly Bonus Schedule 3 or % Improvement

## Slide 3: Profiler Certification Program
Certification Site – Frontage Road off of I-5
Modified Version of AASHTO R 56
ICC SurPRO 3500 Reference Profiler
Certification Site Left Wheelpath IRI ~70
Certification Site Right Wheelpath IRI ~90
ProVAL Profiler Certification Module
ODOT TM 769

## Slide 4: & SPECIFICATIONS
DETERMINING THE INTERNATIONAL ROUGHNESS INDEX WITH AN INERTIAL LASER PROFILER - ODOT TM 772
Calibration Checks
Auto-triggers Required – Start, Stop & Between excluded areas
Measure Right and Left Wheelpaths – MRI for Incentive/Disincentive, Fixed Interval
Localized Roughness Eval on each Wheelpath – 140 in/mile max – Locate Source with 12’ Straightedge.

## Slide 6: Issues
Bounce Test
Lasers Flipped
No funds for Certification Site
Certification

## Slide 7: Issues
How to deal with Ramps & Auxiliary Lanes
Remove and Replace Language
Establishment of Incentive/Disincentive Scales
Specs