## Slide 1: Use of Probe Vehicles to Measure Road Ride Quality
Samer W. Katicha
Senior Research Associate,
Center for Sustainable transportation Infrastructure

## Slide 2: Outline
Smoothness for asset management
Probe vehicles
The experiment
  IRI calculation from profile
  IRI calculation from vertical acceleration measurements
  Sensitivity analysis
Conclusions

## Slide 3: Smoothness for asset managment

## Slide 4: Infrastructure Condition/ Performance Indicators → Pavements
Service and User Perception
Physical Condition
Structural Integrity / Load-Carrying Capacity
Safety and Sufficiency
Environmental Impact
Serviceability (PSI, IRI)
Distress (PCI)
Deflection (FWD)
Friction (FN)/ Macrotexture
Tire/Pav. Noise Rolling Resistance
→ Pavements

## Slide 5: Asset Management
Strategic level
  Performance monitoring
Network level
  Pavement management
Project level
  Smoothness Specification
  Research  LTPP

## Slide 6: Information Quality Levels
Project Level
Strategic Level
Network Level
Performance
Structure
Condition
Ride
Distress
Friction
IQL-5
IQL-4
IQL-3
IQL-2
IQL-1
System
Performance
Monitoring
Planning and
Performance Evaluation
Program Analysis or
Detailed Planning
Project Level or
Detailed Programming
Project Detail or
Research
HIGH LEVEL DATA
LOW LEVEL DATA
Business Processes
Information Quality Levels
Notes: The various IQLs requires different levels of detail and quality in the collected data to support the corresponding decision-making processes, which translate into different methods and frequencies of data collection. Therefore, it is imperative for the determination of data needs to pre-specify the decision level of interest.
The tailoring of the data collected for effective decision-making within the decision level can lead to more specific and focused data collection efforts. This is illustrated in the following section for the project selection decision level.
This plot was adapted from: Bennett, C. and W.D. Paterson, "A Guide to Calibration and Adaptation of HDM-4," in The Highway Development and Management Series, The World Bank, Washington, D.C., 2000.

## Slide 7: Probe Vehicles

## Slide 8: Can we use probe (or regular) vehicles for road infrastructure health monitoring?
At least for supporting high-end strategic- and network-level decisions?

## Slide 9: Pavement Assessment and Management Applications Enabled by the Connected Vehicles Environment – Proof-of-Concept
Objective: To use data collected from probe vehicles to extract information that could be used to remotely and continuously determine road infrastructure health

## Slide 10: The experiment

## Slide 11: Profile and Acceleration Data
Profile data:
  Collected at the Virginia Smart Road
  Every 30 mm (1.2 in)
Probe vehicle acceleration data:
  Collected at the Virginia Smart Road
  Every 2100 mm (7 ft)

## Slide 12: Data Sampling Problem

## Slide 13: Quarter Car Model
kt
kb
Cb

## Slide 14: Quarter Car Model

## Slide 15: Accuracy of Numerical Calculation

## Slide 16: The Probe Vehicle
2007 Ford Fusion
Car parameters:
  Same as golden car
  Close enough
Test Speed:
  50 mph

## Slide 17: IRI Calculation

## Slide 18: IRI Comparisons
Calculated IRI:
  Follow the same trend
  Sample over 2 m makes a difference
Problems with quarter car model:
  Probe vehicle acceleration results from the full car response
  Approximate full car with average of profile felt by the four wheels

## Slide 19: “Full Car” IRI

## Slide 20: Sensitivity Analysis (Sampling)

## Slide 21: Sensitivity Analysis (Quarter Car Parameters)

## Slide 22: Sensitivity Analysis (Sampling)
Suspension Stiffness
Suspension Damping
Tire Stiffness
Mass Ratio

## Slide 23: Conclusions
Same IRI trend between probe vehicle and profiler:
  Effect of data sampling
  Effect of full vs. quarter car
  Effect of probe vehicle car parameters
Use of the data:
  To much uncertainty/variation for detailed analysis
  Maybe useful for strategic level

## Slide 24
Blacksburg, VA