## Slide 1: MSDOT Profiler Certification Program

## Slide 2: General information
Currently certifying for Profilograph Index
Plan to implement MRI Specification and Certification in the next calendar year
Mississippi Contractors’ Profiler Manufacturers include ICC, SSI, and Ames
Must have dual laser system spaced @ 67 to 72 inches
Will be certified annually barring any repair
All operators must be certified with each profiler

## Slide 3: Profiler Certification MSDOT’s Primary Profiler Types:
ICC High Speed Profiler
Pathway High Speed Profiler
ICC SurPRO 3500

## Slide 4: MSDOT’s 3 MRI Categories
Category A
  New construction, three or more lifts, mill and two lifts
Category B
  Mill and one lift, two lift overlays (no milling)
Category C
  Single lift overlay (no milling)
Notes: Categories for first Pilot Project

## Slide 5: MRI Specification Project Categories * The surface smoothness requirements will then be considered a 50% improvement of the existing pavement or 80 in/mile per 0.10-mile segment, whichever is higher.
Pavement Category | Long Continuous Interval Tolerance (in/mile) | Short Continuous Interval Tolerance (in/mile)
A | 60 | 130
B | 70 | 140
C | 50% improvement or 80* | 150

## Slide 6: SMOOTHNESS PAY INCENTIVES
Incentive payments are based upon the Long Continuous MRI scale at intervals of 5 inches/mile
Categories A & B |  | Category C | 
MRI (in/mile) | Price Adjust. (%) | MRI (in/mile) | Price Adjust. (%)
<30.0 | 108 | <30.0 | 103
30.1 to 35.0 | 106 | 30.1 to 35.0 | 103
35.1 to 40.0 | 104 | 35.1 to 40.0 | 103
40.1 to 45.0 | 102 | 40.1 to 45.0 | 103
45.1 to 50.0 | 100 | 45.1 to 50.0 | 100
>60.0 or 70.0 | must correct | >80.0 | must correct
Notes: Pay Incentives for first Pilot Project. Similar to PI pay incentive format.

## Slide 7: Certification sites
Flat, tangent, and wheelpaths marked appropriately
528’ (0.1 miles) in length
Preferably 4 lane non-interstate highway
PAVEMENT TYPES
‘Smooth’ Dense Graded HMA (MRI < 60 in/mile)
‘Rough’ Dense Graded HMA (MRI > 90 in/mile)
Stone Matrix Asphalt
Portland Cement Concrete (Optional)

## Slide 8: TESTING REQUIREMENTS
Based on AASHTO R 56-10
Calibrations include the following: DMI, Block, Bounce, and Accelerometer (if applicable)
Basis Profile established w/ MSDOT’s ICC SurPRO 3500
A minimum of five runs per section for comparison
Data analyzed thru ProVAL’s Profiler Certification Module
Pass/Fail based on 92% Repeatability and 88% Accuracy
All operators will take a written exam

## Slide 9: QA/QC
Collect approximately 10% of jobs annually across the State
Plans to cover all six districts and all contractors evenly
Will use ASTM E950 as basis of comparison
Will ensure Contractors’ profilers are within tolerance throughout the year between certification dates

## Slide 10: Questions?